Mary Gellatly

Dimensions & Regulatory Information:

Length:		100 ft.

Beam:			30 ft.

Depth:			14 ft.

Highest Point:		34 ft.

Man/Min Draft:	13.5 ft. / 13 ft.

Tonnage:		Gross:  187 GRT	Net:  127 NRT

Classification:		American Bureau of Shipping, Loadline Only

Call Sign:		WDA 4911

Official Number:	592075

Home Port:  		New Orleans, LA

ABS ID No.:		7817466

Hull No.:		582

Year Built:		1978

Shipyard:		Halter Marine – New Orleans, LA

Propulsion, Auxillary Machine & Steering:

Main Engines:		CAT D-399 16 Cylinder

Horsepower Total:	2200 BHP

Main Reduction Gears:	Reintjes

Gear Ratio:  		6:1

Propeller:		Fixed Pitch, High Efficiency, 4 Blade

Size, Pitch x Diameter:	100 in. x 76 in.

Generators:		Two (2) GM 6-71

Rating:			75 kw

Rudders:		Two (2)

Tow Drum Wire:	2000 ft. x 1.75 in.

Towing Winch:	Double Drum

Tow Winch Engine:	GM 6-71

Capacities & Delivery Rates:

Fuel Oil:		30,000 USG

Lube Oil Storage:	550 USG

Potable Water:		5,400 USG

Dirty Oil/Slops:	3,000 USG

Features:

Roller Chocks					Cathodic Protection System

Molded Rubber “D” Fendering System	Forward Deck Sheaves

Dutch Bar					Stern Rollers

Stockless Anchor				FM-200 Fire Suppression System in

Engine Room

Electronics:

Chart Plotter with DGPS Interface		Engine Systems Monitor

Northstar GPS					Cell Phone

Fax Machine					2 Radars

E-Mail Capabilities				Furuno Weather Fax

Anemometer					Tow Winch Alarm

Gyro Compass					Auto Pilot

Fathomater					Single-side Band

VHF-FM (4)